## Slide 2
TO THE POINT WITHOUT A PINCH: THE RIGHT WAY TO GUARD
The point of this presentation is to:
Aid in identifying the equipment in your facilities that require guarding
Demonstrate the hazardous areas around that equipment
Learn how to compliantly Guard that equipment with fixed guarding

## Slide 3
STAY AWAY – STAY SAFE
OSHA Regulations & Identifying the Hazards
According to CSA:
Rotating shafts, spindles and couplings:
Guarding of the rotating shafts may be accomplished by means of
fixed guards of solid construction;
bellow-type guards; or
telescopic-type guards
WHY DO WE NEED GUARDING?

## Slide 4
STAY AWAY – STAY SAFE
SAFETY HAZARDS AND WHAT CREATES THEM?
The Point of Operation - the point or location where work is performed on material or where the stock or material is fed into the machine
The Power Transmission Devices – such as flywheels, pulleys, belts, connecting rods, couplings, cams, spindles, chains, cranks and gears.
All Moving Parts - all parts which move while machine is working. Including reciprocating, rotating, and transverse moving parts, feed mechanisms etc.
Please note that this presentation is focused on fixed guarding,
so only the latter two mechanical hazards and how to guard them will be discussed.

## Slide 5
DIRECTION OF BELT TRAVEL
Pinch Point
BELT CONVEYOR IN-RUNNING PINCH POINT
STAY AWAY – STAY SAFE
On Belt Conveyors the in-running pinch point is the area where the belt and roller make contact on the in-feed side.
Notes: 5

## Slide 6
DANGER ZONE KEEP 36” AWAY
36 Inches
36 Inches
36 Inches
DISTANCE FROM DANGER AREA
STAY AWAY – STAY SAFE
Notes: 6

## Slide 7
CONVEYOR BENDS
STAY AWAY – STAY SAFE
The conveyor bend causes pinch points at the return rollers.
The guard is required to be at 36” in all directions from the pinch point and these return rollers are close together,
therefore in this example the guarding is required along the complete conveyor

## Slide 8
FIXED GUARDING
STAY AWAY – STAY SAFE
Fixed Guarding refers to a guard that is a physical barrier between a worker and a danger zone
and it requires a “tool to remove.”

## Slide 9
STAY AWAY – STAY SAFE
There several key points that should always be considered when designing and fitting guards:
The guard should be considered a permanent part of the machine
The guard must make access to all moving parts and nip points physically impossible
The guard should be installed as close to the machine part as possible while still being compliant, be secure, tamper-resistant and durable
The guard must not impede the operation of the plant, and should be designed for the specific job and equipment
The guard itself must not create a new hazard or manual handling risk
The guard must ensure that no object will fall into the moving parts
The guard can only be removed with a tool
The guard must allow for safe lubrication and maintenance
Principles of Fixed Guarding

## Slide 10
STAY AWAY – STAY SAFE
YOUR FIRST LINE OF DEFENCE
A physical barrier (fixed guarding) is a means of physically preventing access to dangerous areas.
It is a requirement by law!

## Slide 11
CONVEYOR HIGH RISK ZONE AREAS
STAY AWAY – STAY SAFE
Tail pulley
Head pulley
Gravity take-ups and counterweights
Snubber pulleys
Additional drive pulleys
V-belt or chain drives
Transfer or load-out points
Skirt boards
Return idlers
Troughing idlers that have obstructions (i.e. ladders)
Conveyor bends
Tripper conveyor
Bearing/Rotating shafts
Couplings
COMMON AREAS REQUIRING GUARDING

## Slide 12
TAIL PULLEYS
STAY AWAY – STAY SAFE
Tail pulley guards should be designed to prevent any contact with:
The pinch point between the pulley and the belt
The exposed pulley and the pulley face
The exposed shaft and bearing

## Slide 13
COUPLINGS
- Exposed shaft & pulley
- Mesh is too large to restrict contact with rotating parts.
- Fully enclosed coupling combined with a Bearing Guard.

## Slide 14
c
V-BELT (Belt Exposed)
V-BELT (Belt Guarded)
V-BELTS
c
STAY AWAY – STAY SAFE
Which situation looks safer to you?

## Slide 15
c
PUMP GUARD
STAY AWAY – STAY SAFE

## Slide 16
Unguarded
Guarded
COUNTER WEIGHT
STAY AWAY – STAY SAFE

## Slide 17
c
c
c
IDLERS
c
STAY AWAY – STAY SAFE
Idlers will need to be guarded to stop someone from making contact or from it potentially falling onto someone.
A pinch point guard is required if anyone is able to reach the hazard.
Idler basket’s primary duty is to catch the roller in case of failure and stop it from falling onto someone that may be walking or driving below at the time.
Notes: ***** CLICK SLIDE *****

## Slide 18
c
FLANGE BEARING
c
STAY AWAY – STAY SAFE
The photo on the left shows an unprotected flange bearing.
Although this shaft may rotate at a slow rate, if a worker were to get entangled, there’s no stopping it.
The photo on the right shows a properly guarded flange bearing. It is designed in such a way as to allow the greasing of the bearing without removal.

## Slide 19
WHEN YOU ARE GUARDING EQUIPMENT YOU MUST NOT BE ABLE TO REACH THE HAZARD FROM
Around
c
c
c
c
Under
Through
Over
A U T O
STAY AWAY – STAY SAFE
The guarding should take into account the physical characteristics of the people involved and, in particular, their abilities to reach through openings and over or around barriers or guards.

## Slide 20
c
HAZARDS THAT ARE NOT RECOGNIZED
UNDER
AROUND
OVER
THROUGH
STAY AWAY – STAY SAFE
Here someone can reach AROUND the guard at the front corner, UNDER the guard from the bottom, THROUGH the guard at the front because the mesh is too close to what is being guarded and OVER the top.
A – U – T – O

## Slide 21
HAZARDS THAT ARE NOT RECOGNIZED
c
c
STAY AWAY – STAY SAFE
Where do you see the hazards here?

## Slide 22
NOW, THIS IS A HAZARD!
c
STAY AWAY – STAY SAFE
What do you see as a guarding concern here?
Exposed Sprocket and Chain
Rotating Parts
Rollers on a track
More?

## Slide 23
WHAT’S MISSING?
c
STAY AWAY – STAY SAFE
Hopefully after today you should never have to witness this.
It definitely required a safety guard!

## Slide 24
NON-COMPLIANT GUARDING VS. COMPLIANT
c
COMPLIANT
NON-COMPLIANT
NON-COMPLIANT
STAY AWAY – STAY SAFE

## Slide 25
c
c
COMPLIANT
NON-COMPLIANT
HAND RAILING VS. GUARDING
STAY AWAY – STAY SAFE

## Slide 26
c
Does the design, material and construction of the guard create a hazard?
IS IT FREE OF:
DOES YOUR GUARD CREATE A HAZARD?
Burrs
Sharp Edges
Pinch Points
STAY AWAY – STAY SAFE

## Slide 27
Use the following checklist to assess your equipment hazards and prioritize your action plans.
For each zone listed, assess your risk rating using the following guidelines:
A = Area is unguarded, hazardous conditions exist and guarding is required for compliance
B = Area that requires frequent maintenance or clean out and guarding needs upgrading
C = Guarding exists but should be improved for compliance
D = Not applicable or no hazards exist
Zones that were identified with an “A or B” risk rating, present imminent danger to workers in the area and need to be addressed immediately.
Zones that have a “C” risk rating should be reviewed with your Supervisors, Workers and your Joint Health & Safety Committee to determine what improvements are required and establish a reasonable time frame for completion.
ASSESS YOUR EQUIPMENT FOR HAZARD RISKS

## Slide 28
SAFETY GAUGE
STAY AWAY – STAY SAFE
Opening size and distance requirements are outlined in
ANSI B.11.19-2019, CSA Z432:23 and ISO 13857-2019 Machine Safety and Safe Distance Standards.
The Machine Safety Gauge is a helpful tool to verify machine safety guarding compliance and ensures that workers are kept safe around rotating equipment and conveyors.

## Slide 29
STAY AWAY – STAY SAFE
DISTANCE FROM POINT OF OPERATION
Please complete the form on our web site to receive a free safety gauge
Distance of guard from hazard according to the guard opening
MAXIMUM OPENING (INCHES) | DISTANCE FROM HAZARD (INCHES)
¼ | 25/32
⅜ | 3 5/32
⅝ | 4 23/32
1¼ | 7 28/32
1⅞ | 33 15/32
5 | Not recommended
Opening size and distance requirements are outlined in
ANSI B.11.19-2019, CSA Z432:23 and ISO 13857-2019 Machine Safety and Safe Distance Standards.

## Slide 30
ANY SPECIAL REQUIREMENTS?
Lubrication
Vibration Analysis
Heat Analysis
Speed Sensing
Corrosive Area
Flammable Area
STAY AWAY – STAY SAFE

## Slide 31
ERGONOMIC & MAINTENANCE-FRIENDLY
STAY AWAY – STAY SAFE
Design your guards to be ergonomic and maintenance-friendly.
CSA states that:
Machinery should be designed to enable all adjustments, lubrication, and maintenance to be carried out without removing the guard or disabling a safety device, and without extensive dismantling of machinery components. When removal of safeguards are required, it shall be conducted under appropriate administrative controls ensuring that;
the work is conducted using procedural controls and alternate safeguarding techniques to control the risk as effectively as possible; and
the safeguards are restored to full operational status, and their operation verified before the machinery is returned to normal service.
**The maintenance and repair crew must never fail to replace the guards before the job is considered finished and the machine is released from lockout.**

## Slide 32
MAINTENANCE-FRIENDLY COUPLING GUARD
c
STAY AWAY – STAY SAFE
This shows how the modular design can be easily disassembled for maintenance.

## Slide 33
Tie Wrap to Lock:
CSA’s Tool to Remove
REMEMBER TO REPLACE THE TIE WRAP
FASTENING SYSTEM
FULLY OPENED POSITION
PARTIALLY OPENED POSITION
PARTIALLY CLOSED POSITION
STAY AWAY – STAY SAFE
Bolts are commonly used as fastening systems but they can rust and often need replacing. Wearing gloves can make it difficult to manipulate them and they can be dropped and lost.
A more user friendly alternative is the Smart Wedge Clamp.
PATENT PENDING

## Slide 34
Locking Wedge Clamp body shows built in set screw
Bird’s eye view of set screw tightened, securing the guards in place
PATENTED
LOCKING WEDGE CLAMP
In open position, set screw allows installation or removal of guards
CLOSED POSITION
STAY AWAY – STAY SAFE
This is designed for applications where using a cable tie is not desirable.
It requires an Allen key to quickly lock or unlock the set screw.

## Slide 35
BENEFITS OF INSPECTION DOORS
c
INSPECTION DOOR = COMPLIANT
c
HOLE CUT IN GUARD = NON-COMPLIANT
c
c
c
STAY AWAY – STAY SAFE
Inspection Doors are necessary when you need to keep machinery running and still want to be able to inspect or access certain areas. The unique 2 piece design allows for retrofitting existing compliant guarding or installing in new.

## Slide 36
INSPECTION DOOR EXTENSIONS
c
c
STAY AWAY – STAY SAFE
This shows you the optional Inspection door extensions which are also available.
They can be customized to suite your application.

## Slide 37
ACCESS PORTS
c
c
STAY AWAY – STAY SAFE
When you need occasional access or continuous and frequent access - use an access port.

## Slide 38
c
HINGED FLAT GUARDS
c
STAY AWAY – STAY SAFE
You may have a need for increased access at times when you are properly locked out.
Hinging certain areas of the guard will allow for easier access to the equipment for maintenance.

## Slide 39
c
A well designed guard should weigh less than 50 pounds.
ERGONOMICS
A guard should not require more than one person to remove or install it.
STAY AWAY – STAY SAFE
Putting weight labels on all guards will ultimately reduce injuries.

## Slide 40
GUARD HANDLES
GUARD SEATS
GUARD HANGERS
ERGONOMIC ACCESSORIES
c
c
c
STAY AWAY – STAY SAFE

## Slide 41
RECOGNITION
Is the Guard recognizable as a “Guard”?
Paint your guards a color which will stand out from your equipment.
Standardize a color which means “Danger”.
Safety Yellow is the most common color.
STAY AWAY – STAY SAFE

## Slide 42: DO YOUR WORKERS KNOW?
EDUCATE YOUR WORKERS
7. What they should do if a guard is damaged or missing. Who they should notify.
5. How to use the safeguarding and why it is required.
4. If their old/existing guarding is compliant to today’s regulations.
3. If there have been any changes to their workspace.
2. How to recognize specific pinch points and rotating hazards in their work space.
1. How to recognize and respect when the equipment needs guarding.
STAY AWAY – STAY SAFE
6. How and under what circumstances, can guards be safely removed and
when the guards must be replaced.

## Slide 43
c
I Thought it Was Stopped!
EDUCATE YOUR WORKERS
WINNER = MACHINE
It Happened So Fast!
STAY AWAY – STAY SAFE
One second or less can change a life and the lives of many, forever.
There is only one winner when an accident happens.

## Slide 44
WHAT IS THE RIPPLE EFFECT?
c
c
STAY AWAY – STAY SAFE
The person who gets hurt or killed is not the only one who is affected by an accident.

## Slide 45
Insurance premiums are likely to rise
Employers deal with rehiring, retraining, costly fines, citations and Workers Compensation
Witnesses may develop PTSD (Post Traumatic Stress Disorder)
Colleagues have increased workload
Family & friends take on extra responsibilities
WORKPLACE
INJURY
RIPPLE EFFECT
STAY AWAY – STAY SAFE
A Workplace Injury can cause a ripple effect.
Who or what do you think is affected?

## Slide 46
ONCE YOU HAVE MADE THE DECISION TO GUARD YOUR ROTATING EQUIPMENT
- BE SURE TO GUARDSMART.
STAY AWAY – STAY SAFE

## Slide 47
Our SUB - BRANDS
STAY AWAY – STAY SAFE

## Slide 48
THANK YOU!